M2M Demo - Lesson #9
DIY Capacitive Sensor

List of components
- ADK board
- Breadboard
- Aluminum foil
- Adhesive tape
- 10 KOhms resistor
- Some wires

Circuit diagram

Arduino code

// Library import
#include <Max3421e.h>
#include <Usb.h>
#include <AndroidAccessory.h>

// Library import Capacitive Sensor
#include <CapacitiveSensor.h>

// CAPACITIVE SENSOR params
#define COMMAND_TOUCH_SENSOR 0x6
// Target value sent to Android
#define SENSOR_ID 0x0
// Capacitive Sensor from which measurements are sent
#define THRESHOLD 50

// Instantiate Capacitive Sensor Object from Capacitive Library (Arduino I/O port used are 4,6)
CapacitiveSensor touchSensor = CapacitiveSensor(4,6);

// Initialize an AndroidAccessory object which implements the Open Accessory protocol.
// Most important params are : Manufacturer, Model and Version.
// They will be used in the Android application to verify that you are communicating with the correct ADK board.
// Additionnally, the URI parameter is used by the Android system to look for an appropriate Android application if none is installed.This can be a link to the Android Market or a product page.
// Ex : AndroidAccessory acc("Manufacturer","Model","Description Demo","Version","URI","Serial");
AndroidAccessory acc("0x0101011101.","M2MDemoKit9", "M2M DemoKit Arduino Board - Lesson #9", "1.0", "", "0000000001234567");

// Buffer for outgoing data
byte sntmsg[3];

void setup() {
  // Set baud rate for serial communication
  Serial.begin(19200);

  acc.powerOn();

  // Disables Auto Calibration
  touchSensor.set_CS_AutocaL_Millis(0xFFFFFFFF);

  // Initialize buffer with Touch Sensor params
  sntmsg[0] = COMMAND_TOUCH_SENSOR;
  sntmsg[1] = SENSOR_ID;
}

void loop() {

  // Is something connected ?
  if(acc.isConnected()) {

    // Takes 30 measurements to reduce false readings and disturbances
    long value = touchSensor.capacitiveSensor(30);

    // Touch Sensor value is superior to fixed THRESHOLD > Send 1
    if (value > THRESHOLD) {
      sntmsg[2] = 0x1;
    } else { // Else send 0
      sntmsg[2] = 0x0;
    }

    // Send buffer to Android
    acc.write (sntmsg,3);
    delay(100);
  }
}

Android code

package com.m2m.projectnine;

import java.io.FileDescriptor;
import java.io.FileInputStream;
import java.io.FileOutputStream;
import java.io.IOException;
import android.media.AudioManager;
import android.media.SoundPool;
import android.os.Bundle;
import android.os.ParcelFileDescriptor;
import android.os.Vibrator;
import android.app.Activity;
import android.app.PendingIntent;
import android.content.BroadcastReceiver;
import android.content.Context;
import android.content.Intent;
import android.content.IntentFilter;
import android.graphics.Color;
import android.util.Log;
import android.widget.LinearLayout;
import android.widget.TextView;
import com.android.future.usb.UsbAccessory;
import com.android.future.usb.UsbManager;
//Use this for Android 3.1+ instead of com.android.future.usb.*
//import android.hardware.usb.UsbAccessory;
//import android.hardware.usb.UsbManager;

public class ProjectNineActivity extends Activity {

// The constant TAG is an identifier for the current class and is used only for logging purposes with logcat.
private static final String TAG = ProjectNineActivity.class.getSimpleName();

// Establishing a connection to an external device has to be permitted by the user.
// When the user is granting the rights to connect your ADK board, the PendingIntent will broadcast the ACTION_USB_PERMISSION with a flag reflecting wheter the user confirmed or denierd the access.
// The boolean variable mPermissionRequestPending is only used to not show the permission dialog again if the user interaction is still pending.
private PendingIntent mPermissionIntent;
private static final String ACTION_USB_PERMISSION = "com.m2m.projectnine.action.USB_PERMISSION";
private boolean mPermissionRequestPending;

// The UsbManager is a system service that manages all interaction with the USB port of the device.
// It is used to enumerate the connected devices and to request and check the permission to connect to an accessory.
// The UsbManager is also responsible for opening the connection to the external device.
private UsbManager mUsbManager;

// The UsbAccessory is a reference to the connected accessory.
private UsbAccessory mAccessory;

// The ParcelFileDescriptor is obtained when the connection to the accessory is established
// It is used to get access to the input- and output stream of the accessory.
private ParcelFileDescriptor mFileDescriptor;
private FileInputStream mInputStream;
private FileOutputStream mOutputStream;

private static final byte COMMAND_TOUCH_SENSOR = 0x6;
private static final byte SENSOR_ID = 0x0;

private LinearLayout linearLayout;
private TextView buzzerIdentifierTextView;

private Vibrator vibrator;
private boolean isVibrating;

private SoundPool soundPool;
private boolean isSoundPlaying;
private int soundId;

private float streamVolumeMax;

/** Called when the activity is first created */
@Override
protected void onCreate(Bundle savedInstanceState) {
super.onCreate(savedInstanceState);

mUsbManager = UsbManager.getInstance(this);
mPermissionIntent = PendingIntent.getBroadcast(this,0, new Intent(ACTION_USB_PERMISSION),0);
IntentFilter filter = new IntentFilter (ACTION_USB_PERMISSION);
filter.addAction(UsbManager.ACTION_USB_ACCESSORY_DETACHED);
registerReceiver(mUsbReceiver, filter);

setContentView(R.layout.main);
linearLayout = (LinearLayout) findViewById(R.id.linear_layout);
buzzerIdentifierTextView = (TextView) findViewById(R.id.buzzer_identifier);

vibrator = ((Vibrator) getSystemService(VIBRATOR_SERVICE));

/*
soundPool = new SoundPool(1, AudioManager.STREAM_MUSIC,0);
soundId = soundPool.load(this, R.raw.daftpunk,1);

AudioManager mgr = (AudioManager) getSystemService(Context.AUDIO_SERVICE);
streamVolumeMax = mgr.getStreamMaxVolume(AudioManager.STREAM_MUSIC);
*/
}

/** Called when the activity is resumed from its paused state and immediately after onCreate() */
@Override
public void onResume() {
super.onResume();

if(mInputStream != null && mOutputStream != null) {
return;
}

UsbAccessory [] accessories = mUsbManager.getAccessoryList();
UsbAccessory accessory = (accessories == null ? null : accessories[0]);
if (accessory !=null) {
if (mUsbManager.hasPermission(accessory)) {
openAccessory(accessory);
} else {
synchronized (mUsbReceiver) {
if(!mPermissionRequestPending) {
mUsbManager.requestPermission(accessory, mPermissionIntent);
mPermissionRequestPending = true;
}
}
}
} else {
Log.d(TAG, "mAccessory is null");
}
}

/** Called when the activity is paused by the system */
@Override
public void onPause() {
super.onPause();
closeAccessory();
stopVibrate();
//stopSound();
}

/** Called when the activity is no longer needed prior to being removed from the activity stack */
@Override
public void onDestroy() {
super.onDestroy();
unregisterReceiver(mUsbReceiver);
//releaseSoundPool();
}

private final BroadcastReceiver mUsbReceiver = new BroadcastReceiver() {

@Override
public void onReceive(Context context, Intent intent) {
String action = intent.getAction();
if (ACTION_USB_PERMISSION.equals(action)) {
synchronized (this) {
UsbAccessory accessory = UsbManager.getAccessory(intent);
if (intent.getBooleanExtra(UsbManager.EXTRA_PERMISSION_GRANTED, false)) {
openAccessory(accessory);
} else {
Log.d(TAG, "permission denied for accessory" + accessory);
}
mPermissionRequestPending = false;
}
} else if (UsbManager.ACTION_USB_ACCESSORY_DETACHED.equals(action)) {
UsbAccessory accessory = UsbManager.getAccessory(intent);
if (accessory != null && accessory.equals(mAccessory)) {
closeAccessory();
}
}
}
};

private void openAccessory(UsbAccessory accessory) {
mFileDescriptor = mUsbManager.openAccessory(accessory);
if (mFileDescriptor != null) {
mAccessory = accessory;
FileDescriptor fd = mFileDescriptor.getFileDescriptor();
mInputStream = new FileInputStream(fd);
mOutputStream = new FileOutputStream(fd);
Thread thread = new Thread(null, commRunnable, TAG);
thread.start();
Log.d(TAG, "accessory opened");
} else {
Log.d(TAG, "accessory open fail");
}
}

private void closeAccessory() {
try {
if (mFileDescriptor != null) {
mFileDescriptor.close();
}
} catch (IOException e) {
} finally {
mFileDescriptor = null;
mAccessory = null;
}
}

Runnable commRunnable = new Runnable() {

@Override
public void run() {
int ret = 0;
byte[] buffer = new byte[3];

while(ret >= 0) {
try {
ret = mInputStream.read(buffer);
} catch (IOException e) {
Log.e(TAG, "IOException : ", e);
break;
}

switch (buffer[0]) {
case COMMAND_TOUCH_SENSOR :
if(buffer[1] == SENSOR_ID) {
final byte buzzerId = buffer[1];
final boolean buzzerIsPressed = buffer[2] == 0x1;

runOnUiThread (new Runnable() {
@Override
public void run() {
if (buzzerIsPressed) {
linearLayout.setBackgroundColor(Color.RED);
buzzerIdentifierTextView.setText(getString(R.string.touch_button_identifier, buzzerId));
startVibrate();
//playSound();
} else {
linearLayout.setBackgroundColor(Color.WHITE);
buzzerIdentifierTextView.setText("");
stopVibrate();
//stopSound();
}
}
});
}
break;

default:
Log.d(TAG, "unknown msg : " + buffer[0]);
break;
}
}
}
};

private void startVibrate() {
if(vibrator != null && !isVibrating) {
isVibrating = true;
vibrator.vibrate(new long[]{0, 1000, 250 },0);
}
}

private void stopVibrate() {
if(vibrator != null && isVibrating) {
isVibrating = false;
vibrator.cancel();
}
}
}

Result