M2M Demo - Lesson #12
SMS Alarm System

List of components
- ADK board
- Breadboard
- 220 Ohms resistor
- 2 x 10 KOhms resistor
- Some wires
- Button
- Tilt-Switch
- LED operating at 5V
- Piezo Buzzer

Circuit diagram

Arduino code

// Library import
#include <Max3421e.h>
#include <Usb.h>
#include <AndroidAccessory.h>

// LED, PIEZO, BUTTON, TILT SWITCH params
#define LED_OUTPUT_PIN 2
#define PIEZO_OUTPUT_PIN 3
#define BUTTON_INPUT_PIN 4
#define TILT_SWITCH_INPUT_PIN 5

// NOTE value define
#define NOTE_C7 2100

// ALARM COMMAND params
#define COMMAND_ALARM 0x9

// ALARM TILT SWITCH params
#define ALARM_TYPE_TILT_SWITCH 0x1

// ALARM Value
#define ALARM_OFF 0x0
#define ALARM_ON 0x1

int tiltSwitchValue;
int buttonValue;
int ledBrightness;
int fadeSteps = 5;

boolean alarm = false;

// Initialize an AndroidAccessory object which implements the Open Accessory protocol.
// Most important params are : Manufacturer, Model and Version.
// They will be used in the Android application to verify that you are communicating with the correct ADK board.
// Additionnally, the URI parameter is used by the Android system to look for an appropriate Android application if none is installed.This can be a link to the Android Market or a product page.
// Ex : AndroidAccessory acc("Manufacturer","Model","Description Demo","Version","URI","Serial");
AndroidAccessory acc("0x0101011101","M2MDemoKit12", "M2M DemoKit Arduino Board - Lesson #12", "1.0", "", "0000000001234567");
// Buffer for outgoing data
byte sntmsg[3];

void setup() {

  // Set baud rate for serial communication
  Serial.begin(19200);

  // Set Arduino I/O #2 to OUTPUT (LED is connected to)
  pinMode(LED_OUTPUT_PIN, OUTPUT);

  // Set Arduino I/O #3 to OUTPUT (PIEZO is connected to)
  pinMode(PIEZO_OUTPUT_PIN, OUTPUT);

  // Set Arduino I/O #4 to INPUT (BUTTON is connected to)
  pinMode(BUTTON_INPUT_PIN, INPUT);

  // Set Arduino I/O #5 to INPUT (TILT SWITCH is connected to)
  pinMode(TILT_SWITCH_INPUT_PIN, INPUT);

  acc.powerOn();

  sntmsg[0] = COMMAND_ALARM;
  sntmsg[1] = ALARM_TYPE_TILT_SWITCH;
}

void loop() {

  // Is something connected ?

  if(acc.isConnected()) {

  // Read current Tilt Switch status
  tiltSwitchValue = digitalRead(TILT_SWITCH_INPUT_PIN);

  // Is Tilt Switch value is HIGH (Something move it)
  if((tiltSwitchValue == HIGH) && !alarm) {
    startAlarm();
  }

  // Alarm ON/OFF Button management
  buttonValue = digitalRead(BUTTON_INPUT_PIN);
  if((buttonValue == LOW) && alarm) {
    stopAlarm();
  }

  // If Alarm, fade LED
  if(alarm) {
    fadeLED();
  }
  delay(10);
  }
}

// Start Alarm function
void startAlarm() {
  alarm = true;

  // Play sound on PIEZO
  tone(PIEZO_OUTPUT_PIN, NOTE_C7);
  ledBrightness = 0;

  // Inform Android device
  sntmsg[2] = ALARM_ON;
  sendAlarmStateMessage();
}

// Stop Alarm function
void stopAlarm() {
  alarm = false;

  // Turn OFF PIEZZO BUZZER
  noTone(PIEZO_OUTPUT_PIN);

  // Turn OFF LED
  digitalWrite(LED_OUTPUT_PIN, LOW);

  // Inform Android device
  sntmsg[2] = ALARM_OFF;
  sendAlarmStateMessage();
}
// Send ALARM status to Android device
void sendAlarmStateMessage() {
  if (acc.isConnected()) {
    acc.write(sntmsg,3);
  }
}

// Manage LED status
void fadeLED() {
  analogWrite(LED_OUTPUT_PIN, ledBrightness);

  // Increase or decrease brightness
  ledBrightness = ledBrightness + fadeSteps;

  // Change fade direction when reaching max or min of analog values
  if (ledBrightness < 0 || ledBrightness > 255) {
    fadeSteps = - fadeSteps;
  }
}

Android code

package com.m2m.projecttwelve;

import java.io.BufferedWriter;
import java.io.File;
import java.io.FileDescriptor;
import java.io.FileInputStream;
import java.io.FileOutputStream;
import java.io.FileWriter;
import java.io.IOException;
import java.text.SimpleDateFormat;
import java.util.Date;
import android.app.Activity;
import android.app.PendingIntent;
import android.app.PendingIntent.CanceledException;
import android.content.BroadcastReceiver;
import android.content.Context;
import android.content.Intent;
import android.content.IntentFilter;
import android.content.pm.PackageManager;
import android.graphics.Color;
import android.os.Bundle;
import android.os.Environment;
import android.os.ParcelFileDescriptor;
import android.telephony.SmsManager;
import android.util.Log;
import android.widget.LinearLayout;
import android.widget.TextView;
import com.android.future.usb.UsbAccessory;
import com.android.future.usb.UsbManager;
//Use this for Android 3.1+ instead of com.android.future.usb.*
//import android.hardware.usb.UsbAccessory;
//import android.hardware.usb.UsbManager;

public class ProjectTwelveActivity extends Activity {

// The constant TAG is an identifier for the current class and is used only for logging purposes with logcat.
private static final String TAG = ProjectTwelveActivity.class.getSimpleName();

// Establishing a connection to an external device has to be permitted by the user.
// When the user is granting the rights to connect your ADK board, the PendingIntent will broadcast the ACTION_USB_PERMISSION with a flag reflecting wheter the user confirmed or denierd the access.
// The boolean variable mPermissionRequestPending is only used to not show the permission dialog again if the user interaction is still pending.
private PendingIntent mPermissionIntent;
private static final String ACTION_USB_PERMISSION = "com.m2m.projecttwelve.action.USB_PERMISSION";
private boolean mPermissionRequestPending;

// The UsbManager is a system service that manages all interaction with the USB port of the device.
// It is used to enumerate the connected devices and to request and check the permission to connect to an accessory.
// The UsbManager is also responsible for opening the connection to the external device.
private UsbManager mUsbManager;

// The UsbAccessory is a reference to the connected accessory.
private UsbAccessory mAccessory;

// The ParcelFileDescriptor is obtained when the connection to the accessory is established
// It is used to get access to the input- and output stream of the accessory.
private ParcelFileDescriptor mFileDescriptor;
private FileInputStream mInputStream;
private FileOutputStream mOutputStream;

// SMS Intent & Log File Intent
private PendingIntent smsSentIntent;
private PendingIntent logFileWrittenIntent;

// Same constants as the ones used in the Arduino sketch.
private static final byte COMMAND_ALARM = 0x9;
private static final byte ALARM_TYPE_TILT_SWITCH = 0x1;
private static final byte ALARM_OFF = 0x0;
private static final byte ALARM_ON = 0x1;

// SMS params
private static final String SMS_DESTINATION = "Mobile phone number to send";
private static final String SMS_SENT_ACTION = "SMS_SENT";
private static final String LOG_FILE_WRITTEN_ACTION = "LOG_FILE_WRITTEN";

private PackageManager packageManager;
boolean hasTelephony;

// The only user-visible UI elements is a Toggle Button & a TextView
private TextView alarmTextView;
private TextView smsTextView;
private TextView logTextView;
private LinearLayout linearLayout;

/** Called when the activity is first created */
@Override
protected void onCreate(Bundle savedInstanceState) {
super.onCreate(savedInstanceState);

// A reference to the USB system service is obtained so that you can call its methods later on
mUsbManager = UsbManager.getInstance(this);

// Use this for Android 3.1+
// mUsbManager = (UsbManager) getSystemService(Context.USB_SERVICE);

// A PendingIntent with the ACTION_USB_PERMISSION parameter is defined
// You will need it when you request the user's permission to connect to a USB device
mPermissionIntent = PendingIntent.getBroadcast(this,0, new Intent(ACTION_USB_PERMISSION),0);

smsSentIntent = PendingIntent.getBroadcast(this, 0, new Intent(SMS_SENT_ACTION), 0);

logFileWrittenIntent = PendingIntent.getBroadcast(this, 0, new Intent(LOG_FILE_WRITTEN_ACTION), 0);

// The intent filter is used in conjunction with a broadcast receiver to make sure that the application only listens to certain broadcasts
IntentFilter filter = new IntentFilter (ACTION_USB_PERMISSION);

// The filter defines that it reacts on the ACTION_USB_PERMISSION action defined as a constant in the beginning and on the ACTION_USB_ACCESSORY_DETACHED action, for when the ADK accessory is disconnected.
filter.addAction(UsbManager.ACTION_USB_ACCESSORY_DETACHED);

filter.addAction(SMS_SENT_ACTION);
filter.addAction(LOG_FILE_WRITTEN_ACTION);

// The registerReceiver method register the broadcast receiver with the described intent filter at the system.
// So when a broadcast is sent by the system, the broadcast receiver will be notified and can take the relevant action.
registerReceiver(mUsbReceiver, filter);

packageManager = getPackageManager();
hasTelephony = packageManager.hasSystemFeature(PackageManager.FEATURE_TELEPHONY);

// Display main content
setContentView(R.layout.main);
linearLayout = (LinearLayout) findViewById(R.id.linear_layout);
alarmTextView = (TextView) findViewById(R.id.alarm_text);
smsTextView = (TextView) findViewById(R.id.sms_text);
logTextView = (TextView) findViewById(R.id.log_text);
}

// Called when the activity is resumed from its paused state and immediately after onCreate()
// It's here you open the connection to your accessory
@Override
public void onResume() {
super.onResume();

// If the input and outputStream is still active you are good to go for communication and can return prematurely
if(mInputStream != null && mOutputStream != null) {
return;
}

// Get reference of the accessory from the UsbManager
UsbAccessory [] accessories = mUsbManager.getAccessoryList();
UsbAccessory accessory = (accessories == null ? null : accessories[0]);

if (accessory !=null) {

// If you already have the user's permission to communicate with the device you can open and reassign the input and output streams
if (mUsbManager.hasPermission(accessory)) {
openAccessory(accessory);
} else {
synchronized (mUsbReceiver) {
if(!mPermissionRequestPending) {
mUsbManager.requestPermission(accessory, mPermissionIntent);
mPermissionRequestPending = true;
}
}
}
} else {
Log.d(TAG, "mAccessory is null");
}
}

// Called when the activity is paused by the system.
// It's here you close the connection to free up memory.
@Override
public void onPause() {
super.onPause();
closeAccessory();
}

// Called when the activity is no longer need to prior to being removed from the activity stack.
// It's here you unregister the BroadcastReceiver
@Override
public void onDestroy() {
super.onDestroy();
unregisterReceiver(mUsbReceiver);
}

// Implementation of the BroadcastReceiver.
    // Anonymous inner class
private final BroadcastReceiver mUsbReceiver = new BroadcastReceiver() {

// Override the onReceive method which is called by the system if this broadcast receiver is registered
// and matches the provided intent-filter.
@Override
public void onReceive(Context context, Intent intent) {

// Check which action occurred when the broadcast receiver is called.
String action = intent.getAction();

// If you receive the action describing that a permission request has been answered
// you will have to check if the user granted permission to communicate with your accessory.
if (ACTION_USB_PERMISSION.equals(action)) {
synchronized (this) {

// Used for Android 2.3
UsbAccessory accessory = UsbManager.getAccessory(intent);

// Use this for Android 3.1+
// UsbAccessory accessory = (UsbAccessory) intent.getParcelableExtra(UsbManager.EXTRA_PERMISSION_GRANTED);

if (intent.getBooleanExtra(UsbManager.EXTRA_PERMISSION_GRANTED, false)) {

// Permission accepted ! We open the communication channels of the accessory !
openAccessory(accessory);

} else {
Log.d(TAG, "permission denied for accessory" + accessory);
}
mPermissionRequestPending = false;
}

// The second action which could have triggered the broadcast receiver
// is the notification that the accessory has been detached from Android device.
} else if (UsbManager.ACTION_USB_ACCESSORY_DETACHED.equals(action)) {

// Use this for Android 2.3.3
UsbAccessory accessory = UsbManager.getAccessory(intent);

// Use this for Android 3.1+
//UsbAccessory accessory = (UsbAccessory) intent.getParcelableExtra(UsbManager.EXTRA_PERMISSION_GRANTED);

if (accessory != null && accessory.equals(mAccessory)) {
closeAccessory();
}
} else if (SMS_SENT_ACTION.equals(action)) {
smsTextView.setText(R.string.sms_sent_message);
} else if (LOG_FILE_WRITTEN_ACTION.equals(action)) {
logTextView.setText(R.string.log_written_message);
}
}
};

// Open the communication channels to the accessory
private void openAccessory(UsbAccessory accessory) {

// Delegate to the USB service method to obtain a FileDescriptor for your accessory.
mFileDescriptor = mUsbManager.openAccessory(accessory);

if (mFileDescriptor != null) {
mAccessory = accessory;

// The FileDescriptor manages the input- output stream used to communicate with your device
FileDescriptor fd = mFileDescriptor.getFileDescriptor();
mInputStream = new FileInputStream(fd);
mOutputStream = new FileOutputStream(fd);
Thread thread = new Thread(null, commRunnable, TAG);
thread.start();
Log.d(TAG, "accessory opened");
} else {
Log.d(TAG, "accessory open fail");
}
}

// Close the communication channels to the accessory
private void closeAccessory() {
try {
if (mFileDescriptor != null) {
mFileDescriptor.close();
}
} catch (IOException e) {
} finally {
mFileDescriptor = null;
mAccessory = null;
}
}

Runnable commRunnable = new Runnable() {

@Override
public void run() {
int ret = 0;
final byte[] buffer = new byte[3];

while(ret >= 0) {
try {
ret = mInputStream.read(buffer);
} catch (IOException e) {
Log.e(TAG, "IOException : ", e);
break;
}

switch (buffer[0]) {
case COMMAND_ALARM :
if(buffer[1] == ALARM_TYPE_TILT_SWITCH) {

final byte alarmState = buffer[2];
final String alarmMessage = getString(R.string.alarm_message, getString(R.string.alarm_type_tilt_switch));

runOnUiThread (new Runnable() {
@Override
public void run() {

linearLayout.setBackgroundColor(buffer[2] == ALARM_ON ? Color.RED : Color.WHITE);
alarmTextView.setText((CharSequence) (buffer[2] == ALARM_ON ? getString(R.string.alarm_message, getString(R.string.alarm_type_tilt_switch)) : R.string.alarm_reset_message));
/*
if (alarmState == ALARM_ON) {
linearLayout.setBackgroundColor(Color.RED);
alarmTextView.setText(alarmMessage);
} else if (alarmState == ALARM_OFF) {
linearLayout.setBackgroundColor(Color.WHITE);
alarmTextView.setText(R.string.alarm_reset_message);
smsTextView.setText("");
logTextView.setText("");
} */
}
});
if (alarmState == ALARM_ON) {
sendSMS(alarmMessage);
SimpleDateFormat dateFormat = new SimpleDateFormat("yyyy-MM-dd-HH-mm-ss");
String currentDateAndTime = dateFormat.format(new Date());
writeToLogFile(new StringBuilder(alarmMessage).append(" - ").append(currentDateAndTime).toString());
}
}
break;

default:
Log.d(TAG, "unknown msg : " + buffer[0]);
break;
}
}
}
};

private void sendSMS(String smsText) {
if(hasTelephony) {
SmsManager smsManager = SmsManager.getDefault();
smsManager.sendTextMessage(SMS_DESTINATION, null, smsText, smsSentIntent, null);
Log.d(TAG, "SMS sent");
}
}

private void writeToLogFile(String logMessage) {
File logDirectory = getExternalLogFilesDir();

if (logDirectory != null) {
File logFile = new File(logDirectory, "ProjectTwelveLog.txt");

if (!logFile.exists()) {
try {
logFile.createNewFile();
} catch (IOException e) {
Log.d(TAG, "Log File could not be created.", e);
}
}

BufferedWriter bufferedWriter = null;

try {
bufferedWriter = new BufferedWriter (new FileWriter(logFile, true));
bufferedWriter.write(logMessage);
bufferedWriter.newLine();
Log.d(TAG, "Written message to file : " + logFile.toURI());
logFileWrittenIntent.send();
} catch (IOException e) {
Log.d(TAG, "Could not write to Log File.", e);
} catch (CanceledException e) {
Log.d(TAG, "LogFileWrittenIntent was cancelled.", e);
} finally {
if (bufferedWriter != null) {
try {
bufferedWriter.close();
} catch (IOException e) {
Log.d(TAG, "Could not close Log File.",e);
}
}
}
}
}

private File getExternalLogFilesDir() {
String state = Environment.getExternalStorageState();
if(Environment.MEDIA_MOUNTED.equals(state)) {
return getExternalFilesDir(null);
} else {
return null;
}
}
}

Result

Move the tilt-switch on breadboard, the first phone (red background) connected to it , detect tilt-switch variation and transmit immediately an alarm to the second smartphone (blue background) through sms.