M2M Demo - Lesson #3
Reading the state of a Button

List of components
- ADK board
- Breadboard
- Button or Switch
- 10 KOhms pull-up resistor
- Some wires

Circuit diagram

Arduino code

// Library import
#include <Max3421e.h>
#include <Usb.h>
#include <AndroidAccessory.h>

// SWITCH params
// Command value received from Android
#define COMMAND_BUTTON 0x1
// Target value received from Android
#define TARGET_BUTTON 0x1
#define VALUE_ON 0x1
#define VALUE_OFF 0x0

// Arduino Board PIN Number on which SWITCH is connected to
#define INPUT_PIN 2

// Initialize an AndroidAccessory object which implements the Open Accessory protocol.
// Most important params are : Manufacturer, Model and Version.
// They will be used in the Android application to verify that you are communicating with the correct ADK board.
// Additionnally, the URI parameter is used by the Android system to look for an appropriate Android application if none is installed.This can be a link to the Android Market or a product page.
// Ex : AndroidAccessory acc("Manufacturer","Model","Description Demo","Version","URI","Serial");
AndroidAccessory acc("0x0101011101","M2MDemoKit3", "M2M DemoKit Arduino Board - Lesson #3", "1.0", "", "0000000001234567");

// Buffer for incoming data
byte sntmsg[3];
int lastButtonState;
int currentButtonState;

void setup() {
  // Set baud rate for serial communication
  Serial.begin(19200);

  acc.powerOn();

  // Initialize buffer value
  sntmsg[0] = COMMAND_BUTTON;
  sntmsg[1] = TARGET_BUTTON;
}

void loop() {

  // Is something connected ?
  if(acc.isConnected()) {

    // Read the current Switch state on PIN #2
    currentButtonState = digitalRead(INPUT_PIN);

    // Compare current state with previous state
    if(currentButtonState != lastButtonState) {
      if(currentButtonState == LOW) {
        sntmsg[2] = VALUE_ON;
      } else {
        sntmsg[2] = VALUE_OFF;
      }
      acc.write(sntmsg,3); // Send Switch state to Android
      lastButtonState = currentButtonState;
    }
    delay(100);
  }
}

Android code

package com.m2m.projectthree;

import java.io.FileDescriptor;
import java.io.FileInputStream;
import java.io.FileOutputStream;
import java.io.IOException;
import android.os.Bundle;
import android.os.ParcelFileDescriptor;
import android.os.Vibrator;
import android.app.Activity;
import android.app.PendingIntent;
import android.content.BroadcastReceiver;
import android.content.Context;
import android.content.Intent;
import android.content.IntentFilter;
import android.util.Log;
import android.widget.TextView;
import com.android.future.usb.UsbAccessory;
import com.android.future.usb.UsbManager;
//Use this for Android 3.1+ instead of com.android.future.usb.*
//import android.hardware.usb.UsbAccessory;
//import android.hardware.usb.UsbManager;

public class ProjectThreeActivity extends Activity {

// The constant TAG is an identifier for the current class and is used only for logging purposes with logcat.
private static final String TAG = ProjectThreeActivity.class.getSimpleName();

// Establishing a connection to an external device has to be permitted by the user.
// When the user is granting the rights to connect your ADK board, the PendingIntent will broadcast the ACTION_USB_PERMISSION with a flag reflecting wheter the user confirmed or denierd the access.
// The boolean variable mPermissionRequestPending is only used to not show the permission dialog again if the user interaction is still pending.
private PendingIntent mPermissionIntent;
private static final String ACTION_USB_PERMISSION = "com.m2m.projectthree.action.USB_PERMISSION";
private boolean mPermissionRequestPending;

// The UsbManager is a system service that manages all interaction with the USB port of the device.
// It is used to enumerate the connected devices and to request and check the permission to connect to an accessory.
// The UsbManager is also responsible for opening the connection to the external device.
private UsbManager mUsbManager;

// The UsbAccessory is a reference to the connected accessory.
private UsbAccessory mAccessory;

// The ParcelFileDescriptor is obtained when the connection to the accessory is established
// It is used to get access to the input- and output stream of the accessory.
private ParcelFileDescriptor mFileDescriptor;
private FileInputStream mInputStream;
private FileOutputStream mOutputStream;

// Same constants as the ones used in the Arduino sketch.
private static final byte COMMAND_BUTTON = 0x1;
private static final byte TARGET_BUTTON = 0x1;
private static final byte VALUE_ON = 0x1;
private static final byte VALUE_OFF = 0x0;

// The only user-visible UI elements is a TextView which should display the button status from the Arduino Board
private static final String BUTTON_PRESSED_TEXT = "The Button is pressed !";
private static final String BUTTON_NOT_PRESSED_TEXT = "The Button is not pressed !";
private TextView buttonStateTextView;

// Android Vibrator service
private Vibrator vibrator;
private boolean isVibrating;

/** Called when the activity is first created */
@Override
protected void onCreate(Bundle savedInstanceState) {
super.onCreate(savedInstanceState);

// A reference to the USB system service is obtained so that you can call its methods later on
mUsbManager = UsbManager.getInstance(this);

// Use this for Android 3.1+
// mUsbManager = (UsbManager) getSystemService(Context.USB_SERVICE);

// A PendingIntent with the ACTION_USB_PERMISSION parameter is defined
// You will need it when you request the user's permission to connect to a USB device
mPermissionIntent = PendingIntent.getBroadcast(this,0, new Intent(ACTION_USB_PERMISSION),0);

// The intent filter is used in conjunction with a broadcast receiver to make sure that the application only listens to certain broadcasts
IntentFilter filter = new IntentFilter (ACTION_USB_PERMISSION);

// The filter defines that it reacts on the ACTION_USB_PERMISSION action defined as a constant in the beginning and on the ACTION_USB_ACCESSORY_DETACHED action, for when the ADK accessory is disconnected.
filter.addAction(UsbManager.ACTION_USB_ACCESSORY_DETACHED);

// The registerReceiver method register the broadcast receiver with the described intent filter at the system.
// So when a broadcast is sent by the system, the broadcast receiver will be notified and can take the relevant action.
registerReceiver(mUsbReceiver, filter);

// Display main content including a TextView for Switch status - Activation of vibrator
setContentView(R.layout.main);
buttonStateTextView = (TextView) findViewById(R.id.button_state_text_view);
vibrator = ((Vibrator) getSystemService(VIBRATOR_SERVICE));
}

// Called when the activity is resumed from its paused state and immediately after onCreate()
// It's here you open the connection to your accessory
@Override
public void onResume() {
super.onResume();

// If the input and outputStream is still active you are good to go for communication and can return prematurely
if(mInputStream != null && mOutputStream != null) {
return;
}

// Get reference of the accessory from the UsbManager
UsbAccessory [] accessories = mUsbManager.getAccessoryList();
UsbAccessory accessory = (accessories == null ? null : accessories[0]);

if (accessory !=null) {

// If you already have the user's permission to communicate with the device you can open and reassign the input and output streams
if (mUsbManager.hasPermission(accessory)) {
openAccessory(accessory);
} else {
synchronized (mUsbReceiver) {
if(!mPermissionRequestPending) {
mUsbManager.requestPermission(accessory, mPermissionIntent);
mPermissionRequestPending = true;
}
}
}
} else {
Log.d(TAG, "mAccessory is null");
}
}

// Called when the activity is paused by the system.
// It's here you close the connection to free up memory.
@Override
public void onPause() {
super.onPause();
closeAccessory();
stopVibrate();
}

// Called when the activity is no longer need to prior to being removed from the activity stack.
// It's here you unregister the BroadcastReceiver
@Override
public void onDestroy() {
super.onDestroy();
stopVibrate();
unregisterReceiver(mUsbReceiver);
}

// Implementation of the BroadcastReceiver.
    // Anonymous inner class
private final BroadcastReceiver mUsbReceiver = new BroadcastReceiver() {

@Override
public void onReceive(Context context, Intent intent) {

// Check which action occurred when the broadcast receiver is called.
String action = intent.getAction();

// If you receive the action describing that a permission request has been answered
// you will have to check if the user granted permission to communicate with your accessory.
if (ACTION_USB_PERMISSION.equals(action)) {
synchronized (this) {

// Used for Android 2.3
UsbAccessory accessory = UsbManager.getAccessory(intent);

// Use this for Android 3.1+
// UsbAccessory accessory = (UsbAccessory) intent.getParcelableExtra(UsbManager.EXTRA_PERMISSION_GRANTED);

if (intent.getBooleanExtra(UsbManager.EXTRA_PERMISSION_GRANTED, false)) {

// Permission accepted ! We open the communication channels of the accessory !
openAccessory(accessory);

} else {
Log.d(TAG, "permission denied for accessory" + accessory);
}
mPermissionRequestPending = false;
}

// The second action which could have triggered the broadcast receiver
// is the notification that the accessory has been detached from Android device.
} else if (UsbManager.ACTION_USB_ACCESSORY_DETACHED.equals(action)) {

// Use this for Android 2.3.3
UsbAccessory accessory = UsbManager.getAccessory(intent);

// Use this for Android 3.1+
//UsbAccessory accessory = (UsbAccessory) intent.getParcelableExtra(UsbManager.EXTRA_PERMISSION_GRANTED);

if (accessory != null && accessory.equals(mAccessory)) {
closeAccessory();
}
}
}
};

// Open the communication channels to the accessory
private void openAccessory(UsbAccessory accessory) {

// Delegate to the USB service method to obtain a FileDescriptor for your accessory.
mFileDescriptor = mUsbManager.openAccessory(accessory);
if (mFileDescriptor != null) {
mAccessory = accessory;

// The FileDescriptor manages the input- output stream used to communicate with your device
FileDescriptor fd = mFileDescriptor.getFileDescriptor();
mInputStream = new FileInputStream(fd);
mOutputStream = new FileOutputStream(fd);
Thread thread = new Thread(null, commRunnable, TAG);
thread.start();
Log.d(TAG, "accessory opened");
} else {
Log.d(TAG, "accessory open fail");
}
}

// Close the communication channels to the accessory
private void closeAccessory() {
try {
if (mFileDescriptor != null) {
mFileDescriptor.close();
}
} catch (IOException e) {
} finally {
mFileDescriptor = null;
mAccessory = null;
}
}

// Thread which manage buffer input from Switch on Arduino board, activate Android vibrator and display Switch text status
Runnable commRunnable = new Runnable() {
@Override
public void run() {
int ret = 0;
final byte[] buffer = new byte[3];

while(ret >=0) {

try {
ret = mInputStream.read(buffer);
} catch (IOException e) {
Log.e(TAG, "IOException : ", e);
break;
}

switch (buffer[0]) {

case COMMAND_BUTTON :
if(buffer[1] == TARGET_BUTTON) {
if(buffer[2] == VALUE_ON) {
startVibrate();
} else if (buffer[2] == VALUE_OFF) {
stopVibrate();
}
runOnUiThread(new Runnable() {

@Override
public void run() {
buttonStateTextView.setText(buffer[2] == VALUE_ON ? BUTTON_PRESSED_TEXT : BUTTON_NOT_PRESSED_TEXT);
}
});
}
break;

default :
Log.d(TAG, "unknown msg : " + buffer[0]);
break;
}
}
}
};

// Start Vibrator function
public void startVibrate() {
if (vibrator != null && !isVibrating) {
isVibrating = true;
vibrator.vibrate(new long[] {0,1000,250},0);
}
}

// Stop Vibrator function
public void stopVibrate() {
if (vibrator != null && isVibrating) {
isVibrating = false;
vibrator.cancel();
}
}
}
Android Manifest.xml

Don't forget to add permission for the vibrator

<?xml version="1.0" encoding="utf-8"?>
<manifest xmlns:android="http://schemas.android.com/apk/res/android"
    package="com.m2m.projectthree"
    android:versionCode="1"
    android:versionName="1.0" >

    <uses-sdk
        android:minSdkVersion="10"
        android:maxSdkVersion="17"
        android:targetSdkVersion="17" />

    <uses-feature android:name="android.hardware.usb.accessory" />

    <uses-permission android:name="android.permission.VIBRATE" />

    <application
        android:allowBackup="true"
        android:icon="@drawable/ic_launcher"
        android:label="@string/app_name"
        android:theme="@style/MyAppTheme" >

        <uses-library android:name="com.android.future.usb.accessory"/>

        <activity
        android:name="com.m2m.projectthree.ProjectThreeActivity"
        android:label="@string/app_name"
        android:screenOrientation="portrait">
        <intent-filter>
        <action android:name="android.intent.action.MAIN" />
        <category android:name="android.intent.category.LAUNCHER" />
        </intent-filter>
        <intent-filter>
        <action android:name="android.hardware.usb.action.USB_ACCESSORY_ATTACHED"/>
        </intent-filter>
        <meta-data android:name="android.hardware.usb.action.USB_ACCESSORY_ATTACHED" android:resource="@xml/accessory_filter"/>
        </activity>
    </application>

</manifest>

Result

When you press the button, the smartphone vibrate