M2M Demo - Lesson #7
Light Intensity Sensing

List of components
- ADK board
- Breadboard
- Photoresistor
- 10 KOhms resistor
- Some wires

Circuit diagram

Arduino code

// Library import
#include <Max3421e.h>
#include <Usb.h>
#include <AndroidAccessory.h>

// LIGHT SENSOR params
// Command value received from Android
#define COMMAND_LIGHT_INTENSITY 0x5
// Target value received from Android
#define INPUT_PIN_0 0x0

// Initialize an AndroidAccessory object which implements the Open Accessory protocol.
// Most important params are : Manufacturer, Model and Version.
// They will be used in the Android application to verify that you are communicating with the correct ADK board.
// Additionnally, the URI parameter is used by the Android system to look for an appropriate Android application if none is installed.This can be a link to the Android Market or a product page.
// Ex : AndroidAccessory acc("Manufacturer","Model","Description Demo","Version","URI","Serial");
AndroidAccessory acc("0x0101011101","M2MDemoKit7", "M2M DemoKit Arduino Board - Lesson #7", "1.0", "", "0000000001234567");

// Buffer for outgoing data
byte sntmsg[3];

void setup() {
  // Set baud rate for serial communication
  Serial.begin(19200);

  acc.powerOn();

  sntmsg[0] = COMMAND_LIGHT_INTENSITY;
  sntmsg[1] = INPUT_PIN_0;
}

void loop() {

  // Is something connected ?
  if(acc.isConnected()) {

    // Read LIGHT SENSOR Analog Value
    int currentValue = analogRead(INPUT_PIN_0);

    // Analog > Digital mapping currentValue
    sntmsg[2] = map (currentValue, 0, 1023, 0, 255);

    // Send to Android
    acc.write (sntmsg,3);
    delay(100);
  }
}

Android code

package com.m2m.projectseven;

import java.io.FileDescriptor;
import java.io.FileInputStream;
import java.io.FileOutputStream;
import java.io.IOException;
import android.os.Bundle;
import android.os.ParcelFileDescriptor;
import android.app.Activity;
import android.app.PendingIntent;
import android.content.BroadcastReceiver;
import android.content.Context;
import android.content.Intent;
import android.content.IntentFilter;
import android.util.Log;
import android.view.WindowManager.LayoutParams;
import android.widget.TextView;
import com.android.future.usb.UsbAccessory;
import com.android.future.usb.UsbManager;
//Use this for Android 3.1+ instead of com.android.future.usb.*
//import android.hardware.usb.UsbAccessory;
//import android.hardware.usb.UsbManager;

public class ProjectSevenActivity extends Activity {

// The constant TAG is an identifier for the current class and is used only for logging purposes with logcat.
private static final String TAG = ProjectSevenActivity.class.getSimpleName();

// Establishing a connection to an external device has to be permitted by the user.
// When the user is granting the rights to connect your ADK board, the PendingIntent will broadcast the ACTION_USB_PERMISSION with a flag reflecting wheter the user confirmed or denierd the access.
// The boolean variable mPermissionRequestPending is only used to not show the permission dialog again if the user interaction is still pending.
private PendingIntent mPermissionIntent;
private static final String ACTION_USB_PERMISSION = "com.m2m.projectseven.action.USB_PERMISSION";
private boolean mPermissionRequestPending;

// The UsbManager is a system service that manages all interaction with the USB port of the device.
// It is used to enumerate the connected devices and to request and check the permission to connect to an accessory.
// The UsbManager is also responsible for opening the connection to the external device.
private UsbManager mUsbManager;

// The UsbAccessory is a reference to the connected accessory.
private UsbAccessory mAccessory;

// The ParcelFileDescriptor is obtained when the connection to the accessory is established
// It is used to get access to the input- and output stream of the accessory.
private ParcelFileDescriptor mFileDescriptor;
private FileInputStream mInputStream;
private FileOutputStream mOutputStream;

// Same constants as the ones used in the Arduino sketch.
private static final byte COMMAND_LIGHT_INTENSITY = 0x5;
private static final byte TARGET_PIN = 0x0;

// The only user-visible UI elements is a TextView and a LayoutParams
private TextView lightIntensityTextView;
private LayoutParams windowLayoutParams;

/** Called when the activity is first created */
@Override
protected void onCreate(Bundle savedInstanceState) {
super.onCreate(savedInstanceState);

// A reference to the USB system service is obtained so that you can call its methods later on
mUsbManager = UsbManager.getInstance(this);

// Use this for Android 3.1+
// mUsbManager = (UsbManager) getSystemService(Context.USB_SERVICE);

// A PendingIntent with the ACTION_USB_PERMISSION parameter is defined
// You will need it when you request the user's permission to connect to a USB device
mPermissionIntent = PendingIntent.getBroadcast(this,0, new Intent(ACTION_USB_PERMISSION),0);

// The intent filter is used in conjunction with a broadcast receiver to make sure that the application only listens to certain broadcasts
IntentFilter filter = new IntentFilter (ACTION_USB_PERMISSION);

// The filter defines that it reacts on the ACTION_USB_PERMISSION action defined as a constant in the beginning and on the ACTION_USB_ACCESSORY_DETACHED action, for when the ADK accessory is disconnected.
filter.addAction(UsbManager.ACTION_USB_ACCESSORY_DETACHED);

// The registerReceiver method register the broadcast receiver with the described intent filter at the system.
// So when a broadcast is sent by the system, the broadcast receiver will be notified and can take the relevant action.
registerReceiver(mUsbReceiver, filter);

// Display main content including a TextView
setContentView(R.layout.main);
lightIntensityTextView = (TextView) findViewById(R.id.light_intensity_text_view);
}

// Called when the activity is resumed from its paused state and immediately after onCreate()
// It's here you open the connection to your accessory
@Override
public void onResume() {
super.onResume();

// If the input and outputStream is still active you are good to go for communication and can return prematurely
if(mInputStream != null && mOutputStream != null) {
return;
}

// Get reference of the accessory from the UsbManager
UsbAccessory [] accessories = mUsbManager.getAccessoryList();
UsbAccessory accessory = (accessories == null ? null : accessories[0]);

if (accessory !=null) {

// If you already have the user's permission to communicate with the device you can open and reassign the input and output streams
if (mUsbManager.hasPermission(accessory)) {
openAccessory(accessory);
} else {
synchronized (mUsbReceiver) {
if(!mPermissionRequestPending) {
mUsbManager.requestPermission(accessory, mPermissionIntent);
mPermissionRequestPending = true;
}
}
}
} else {
Log.d(TAG, "mAccessory is null");
}
}

// Called when the activity is paused by the system.
// It's here you close the connection to free up memory.
@Override
public void onPause() {
super.onPause();
closeAccessory();
}

// Called when the activity is no longer need to prior to being removed from the activity stack.
// It's here you unregister the BroadcastReceiver
@Override
public void onDestroy() {
super.onDestroy();
unregisterReceiver(mUsbReceiver);
}

// Implementation of the BroadcastReceiver.
    // Anonymous inner class
private final BroadcastReceiver mUsbReceiver = new BroadcastReceiver() {

// Override the onReceive method which is called by the system if this broadcast receiver is registered
// and matches the provided intent-filter.
@Override
public void onReceive(Context context, Intent intent) {

// Check which action occurred when the broadcast receiver is called.
String action = intent.getAction();

// If you receive the action describing that a permission request has been answered
// you will have to check if the user granted permission to communicate with your accessory.
if (ACTION_USB_PERMISSION.equals(action)) {
synchronized (this) {

// Used for Android 2.3
UsbAccessory accessory = UsbManager.getAccessory(intent);

// Use this for Android 3.1+
// UsbAccessory accessory = (UsbAccessory) intent.getParcelableExtra(UsbManager.EXTRA_PERMISSION_GRANTED);

if (intent.getBooleanExtra(UsbManager.EXTRA_PERMISSION_GRANTED, false)) {

// Permission accepted ! We open the communication channels of the accessory !
openAccessory(accessory);

} else {
Log.d(TAG, "permission denied for accessory" + accessory);
}
mPermissionRequestPending = false;
}

// The second action which could have triggered the broadcast receiver
// is the notification that the accessory has been detached from Android device.
} else if (UsbManager.ACTION_USB_ACCESSORY_DETACHED.equals(action)) {

// Use this for Android 2.3.3
UsbAccessory accessory = UsbManager.getAccessory(intent);

// Use this for Android 3.1+
//UsbAccessory accessory = (UsbAccessory) intent.getParcelableExtra(UsbManager.EXTRA_PERMISSION_GRANTED);

if (accessory != null && accessory.equals(mAccessory)) {
closeAccessory();
}
}
}
};

// Open the communication channels to the accessory
private void openAccessory(UsbAccessory accessory) {

// Delegate to the USB service method to obtain a FileDescriptor for your accessory.
mFileDescriptor = mUsbManager.openAccessory(accessory);
if (mFileDescriptor != null) {
mAccessory = accessory;

// The FileDescriptor manages the input- output stream used to communicate with your device
FileDescriptor fd = mFileDescriptor.getFileDescriptor();
mInputStream = new FileInputStream(fd);
mOutputStream = new FileOutputStream(fd);
Thread thread = new Thread(null, commRunnable, TAG);
thread.start();
Log.d(TAG, "accessory opened");
} else {
Log.d(TAG, "accessory open fail");
}
}

// Close the communication channels to the accessory
private void closeAccessory() {
try {
if (mFileDescriptor != null) {
mFileDescriptor.close();
}
} catch (IOException e) {
} finally {
mFileDescriptor = null;
mAccessory = null;
}
}

// Read analog value from ADK Board
Runnable commRunnable = new Runnable() {

@Override
public void run() {
int ret = 0;
byte[] buffer = new byte[3];

while(ret >= 0) {

try {
ret = mInputStream.read(buffer);
} catch (IOException e) {
Log.e(TAG, "IOException : ", e);
break;
}

switch (buffer[0]) {
case COMMAND_LIGHT_INTENSITY :
if(buffer[1] == TARGET_PIN) {
final byte lightIntensityValue = buffer[2];

runOnUiThread (new Runnable() {
@Override
public void run() {
lightIntensityTextView.setText(getString(R.string.light_intensity_value, lightIntensityValue));
windowLayoutParams = getWindow().getAttributes();
windowLayoutParams.screenBrightness = lightIntensityValue / 100.0f;
getWindow().setAttributes(windowLayoutParams);
}
});
}
break;

default:
Log.d(TAG, "unknown msg : " + buffer[0]);
break;
}
}
}
};
}

Result