M2M Demo - Lesson #13
Camera Alarm System

List of components
- ADK board
- Breadboard
- 3 X 220 Ohms resistor
- 2 x 10 KOhms resistor
- Some wires
- Button
- IR light barrier (IR emitter, IR detector)
- LED operating at 5V
- Piezo Buzzer

Circuit diagram

Arduino code

// Library import
#include <Max3421e.h>
#include <Usb.h>
#include <AndroidAccessory.h>

// LED, PIEZO, BUTTON, IR LIGHT BARRIER input PIN
#define BUTTON_INPUT_PIN 2
#define PIEZO_OUTPUT_PIN 3
#define LED_ALARM_ON_PIN 4
#define LED_ALARM_OFF_PIN 5
#define IR_LIGHT_BARRIER_INPUT_PIN A0

// IR LIGHT THRESHOLD value >> WARNING : Depend on IR Receiver / Emitter LED models params (cf datasheet) - Receiver & Emitter must have same frequencies
#define IR_LIGHT_BARRIER_THRESHOLD 260

// NOTE value define
#define NOTE_C7 2100

// ALARM COMMAND params
#define COMMAND_ALARM 0x9

// ALARM TYPE IR LIGHT BARRIER COMMAND value
#define ALARM_TYPE_IR_LIGHT_BARRIER 0x2

// ALARM ON/OFF Value
#define ALARM_OFF 0x0
#define ALARM_ON 0x1

int irLightBarrierValue;
int buttonValue;
int ledBrightness = 0;

boolean alarm = false;

// Initialize an AndroidAccessory object which implements the Open Accessory protocol.
// Most important params are : Manufacturer, Model and Version.
// They will be used in the Android application to verify that you are communicating with the correct ADK board.
// Additionnally, the URI parameter is used by the Android system to look for an appropriate Android application if none is installed.This can be a link to the Android Market or a product page.
// Ex : AndroidAccessory acc("Manufacturer","Model","Description Demo","Version","URI","Serial");
AndroidAccessory acc("0x0101011101","M2MDemoKit13", "M2M DemoKit Arduino Board - Lesson #13", "1.0", "", "0000000001234567");

// Buffer for outgoing data
byte sntmsg[3];

void setup() {

  // Set baud rate for serial communication
  Serial.begin(9600);

  // Set Arduino I/O #2 to OUTPUT (LED is connected to)
  pinMode(LED_ALARM_ON_PIN, OUTPUT);

  // Set Arduino I/O #5 to OUTPUT (LED is connected to)
  pinMode(LED_ALARM_OFF_PIN, OUTPUT);

  // Set Arduino I/O #4 to INPUT (BUTTON is connected to)
  pinMode(BUTTON_INPUT_PIN, INPUT);

  digitalWrite(LED_ALARM_OFF_PIN, HIGH);

  acc.powerOn();
}

void loop() {

  // Is something connected ?
  if (acc.isConnected()) {

    // Read current IR LED status
    irLightBarrierValue = analogRead(IR_LIGHT_BARRIER_INPUT_PIN);

    Serial.println(irLightBarrierValue);
    delay(1500);

    // Is IR LED value is superior to Threshold & Alarm is not ON ?
    if ((irLightBarrierValue < IR_LIGHT_BARRIER_THRESHOLD) && !alarm) {
      startAlarm();
    }

    // Alarm ON/OFF Button management
    buttonValue = digitalRead(BUTTON_INPUT_PIN);
    Serial.println(buttonValue);
    if((buttonValue == LOW) && alarm) {
      stopAlarm();
    }
  }
}

// Start Alarm function
void startAlarm() {

  alarm = true;

  // Play sound on PIEZO
  tone(PIEZO_OUTPUT_PIN, NOTE_C7);

  // TURN OFF Alarm Green LED
  digitalWrite(LED_ALARM_OFF_PIN, LOW);
  // TURN ON Alarm Red LED
  digitalWrite(LED_ALARM_ON_PIN, HIGH);

  // Inform Android device
  sntmsg[2] = ALARM_ON;
  sendAlarmStateMessage();
}

// Stop Alarm function
void stopAlarm() {

  alarm = false;

  // Turn OFF PIEZZO BUZZER
  noTone(PIEZO_OUTPUT_PIN);

  // Turn OFF Alarm Red LED
  digitalWrite(LED_ALARM_ON_PIN, LOW);
  // TURN ON Alarm Green LED
  digitalWrite(LED_ALARM_OFF_PIN, HIGH);

  // Inform Android device
  sntmsg[2] = ALARM_OFF;
  sendAlarmStateMessage();
}

// Send ALARM status to Android device
void sendAlarmStateMessage() {
  if (acc.isConnected()) {
    sntmsg[0] = COMMAND_ALARM;
    sntmsg[1] = ALARM_TYPE_IR_LIGHT_BARRIER;
    acc.write(sntmsg,3);
  }
}

Android code

package com.m2m.projectthirteen;

import java.io.BufferedOutputStream;
import java.io.BufferedWriter;
import java.io.File;
import java.io.FileDescriptor;
import java.io.FileInputStream;
import java.io.FileOutputStream;
import java.io.FileWriter;
import java.io.IOException;
import java.text.SimpleDateFormat;
import java.util.Date;
import android.app.Activity;
import android.app.PendingIntent;
import android.app.PendingIntent.CanceledException;
import android.content.BroadcastReceiver;
import android.content.Context;
import android.content.Intent;
import android.content.IntentFilter;
import android.content.pm.PackageManager;
import android.graphics.Color;
import android.hardware.Camera;
import android.hardware.Camera.CameraInfo;
import android.hardware.Camera.PictureCallback;
import android.os.Bundle;
import android.os.Environment;
import android.os.ParcelFileDescriptor;
import android.util.Log;
import android.view.SurfaceView;
import android.widget.FrameLayout;
import android.widget.LinearLayout;
import android.widget.TextView;
import com.android.future.usb.UsbAccessory;
import com.android.future.usb.UsbManager;
//Use this for Android 3.1+ instead of com.android.future.usb.*
//import android.hardware.usb.UsbAccessory;
//import android.hardware.usb.UsbManager;

public class ProjectThirteenActivity extends Activity {

// The constant TAG is an identifier for the current class and is used only for logging purposes with logcat.
private static final String TAG = ProjectThirteenActivity.class.getSimpleName();

// Establishing a connection to an external device has to be permitted by the user.
// When the user is granting the rights to connect your ADK board, the PendingIntent will broadcast the ACTION_USB_PERMISSION with a flag reflecting wheter the user confirmed or denierd the access.
// The boolean variable mPermissionRequestPending is only used to not show the permission dialog again if the user interaction is still pending.
private PendingIntent mPermissionIntent;
private static final String ACTION_USB_PERMISSION = "com.m2m.projectthirteen.action.USB_PERMISSION";
private boolean mPermissionRequestPending;

// The UsbManager is a system service that manages all interaction with the USB port of the device.
// It is used to enumerate the connected devices and to request and check the permission to connect to an accessory.
// The UsbManager is also responsible for opening the connection to the external device.
private UsbManager mUsbManager;

// The UsbAccessory is a reference to the connected accessory.
private UsbAccessory mAccessory;

// The ParcelFileDescriptor is obtained when the connection to the accessory is established
// It is used to get access to the input- and output stream of the accessory.
private ParcelFileDescriptor mFileDescriptor;
private FileInputStream mInputStream;
private FileOutputStream mOutputStream;

// SMS Intent & Log File Intent
private PendingIntent photoTakenIntent;
private PendingIntent logFileWrittenIntent;

// Same constants as the ones used in the Arduino sketch.
private static final byte COMMAND_ALARM = 0x9;
private static final byte ALARM_TYPE_IR_LIGHT_BARRIER = 0x2;
private static final byte ALARM_OFF = 0x0;
private static final byte ALARM_ON = 0x1;

private static final String PHOTO_TAKEN_ACTION = "PHOTO_TAKEN";
private static final String LOG_FILE_WRITTEN_ACTION = "LOG_FILE_WRITTEN";

// Create PackageManager instance to find global package information.
private PackageManager packageManager;

// Boolean to test if smartphone has 1 or 2 camera
private boolean hasFrontCamera;
private boolean hasBackCamera;

// Camera params
private Camera camera;
private SurfaceView surfaceView;

// The only user-visible UI elements are TextView, LinearLayout & FrameLayout
private TextView alarmTextView;
private TextView photoTakenTextView;
private TextView logTextView;
private LinearLayout linearLayout;
private FrameLayout frameLayout;

/** Called when the activity is first created */
@Override
protected void onCreate(Bundle savedInstanceState) {
super.onCreate(savedInstanceState);

// A reference to the USB system service is obtained so that you can call its methods later on
mUsbManager = UsbManager.getInstance(this);

// Use this for Android 3.1+
// mUsbManager = (UsbManager) getSystemService(Context.USB_SERVICE);

// A PendingIntent with the ACTION_USB_PERMISSION parameter is defined
// You will need it when you request the user's permission to connect to a USB device
mPermissionIntent = PendingIntent.getBroadcast(this,0, new Intent(ACTION_USB_PERMISSION),0);

// A PendingIntent with the PHOTO_TAKEN_ACTION parameter is defined
photoTakenIntent = PendingIntent.getBroadcast(this, 0, new Intent(PHOTO_TAKEN_ACTION), 0);

// A PendingIntent with the LOG_FILE_WRITTEN_ACTION parameter is defined
logFileWrittenIntent = PendingIntent.getBroadcast(this, 0, new Intent(LOG_FILE_WRITTEN_ACTION), 0);

// The intent filter is used in conjunction with a broadcast receiver to make sure that the application only listens to certain broadcasts
IntentFilter filter = new IntentFilter (ACTION_USB_PERMISSION);

// The filter defines that it reacts on the ACTION_USB_PERMISSION action defined as a constant in the beginning and on the ACTION_USB_ACCESSORY_DETACHED action, for when the ADK accessory is disconnected.
filter.addAction(UsbManager.ACTION_USB_ACCESSORY_DETACHED);

// The filter defines that it reacts on the PHOTO_TAKEN_ACTION action defined
filter.addAction(PHOTO_TAKEN_ACTION);

// The filter defines that it reacts on the LOG_FILE_WRITTEN_ACTION action defined
filter.addAction(LOG_FILE_WRITTEN_ACTION);

// The registerReceiver method register the broadcast receiver with the described intent filter at the system.
// So when a broadcast is sent by the system, the broadcast receiver will be notified and can take the relevant action.
registerReceiver(mUsbReceiver, filter);

// Find global package information
packageManager = getPackageManager();

// To count how much camera the smartphone has
hasFrontCamera = packageManager.hasSystemFeature(PackageManager.FEATURE_CAMERA_FRONT);
hasBackCamera = packageManager.hasSystemFeature(PackageManager.FEATURE_CAMERA);

// Display main content
setContentView(R.layout.main);

// UI params
linearLayout = (LinearLayout) findViewById(R.id.linear_layout);
frameLayout = (FrameLayout) findViewById(R.id.camera_preview);
alarmTextView = (TextView) findViewById(R.id.alarm_text);
photoTakenTextView = (TextView) findViewById(R.id.photo_taken_text);
logTextView = (TextView) findViewById(R.id.log_text);
}

// Called when the activity is resumed from its paused state and immediately after onCreate()
// It's here you open the connection to your accessory
@Override
public void onResume() {
super.onResume();

// Classic Camera initialization
camera = getCamera();
surfaceView = new CameraPreview(this,camera);
frameLayout.addView(surfaceView);

// If the input and outputStream is still active you are good to go for communication and can return prematurely
if(mInputStream != null && mOutputStream != null) {
return;
}

// Get reference of the accessory from the UsbManager
UsbAccessory [] accessories = mUsbManager.getAccessoryList();
UsbAccessory accessory = (accessories == null ? null : accessories[0]);

if (accessory !=null) {

// If you already have the user's permission to communicate with the device you can open and reassign the input and output streams
if (mUsbManager.hasPermission(accessory)) {
openAccessory(accessory);
} else {
synchronized (mUsbReceiver) {
if(!mPermissionRequestPending) {
mUsbManager.requestPermission(accessory, mPermissionIntent);
mPermissionRequestPending = true;
}
}
}
} else {
Log.d(TAG, "mAccessory is null");
}
}

// Called when the activity is paused by the system.
// It's here you close the connection to free up memory.
@Override
public void onPause() {
super.onPause();
closeAccessory();

if(camera != null) {
camera.release();
camera = null;
frameLayout.removeAllViews();
}
}

// Called when the activity is no longer need to prior to being removed from the activity stack.
// It's here you unregister the BroadcastReceiver
@Override
public void onDestroy() {
super.onDestroy();
unregisterReceiver(mUsbReceiver);
}

// Implementation of the BroadcastReceiver.
    // Anonymous inner class
private final BroadcastReceiver mUsbReceiver = new BroadcastReceiver() {

// Override the onReceive method which is called by the system if this broadcast receiver is registered
// and matches the provided intent-filter.
@Override
public void onReceive(Context context, Intent intent) {

// Check which action occurred when the broadcast receiver is called.
String action = intent.getAction();

// If you receive the action describing that a permission request has been answered
// you will have to check if the user granted permission to communicate with your accessory.
if (ACTION_USB_PERMISSION.equals(action)) {
synchronized (this) {

// Used for Android 2.3
UsbAccessory accessory = UsbManager.getAccessory(intent);

// Use this for Android 3.1+
// UsbAccessory accessory = (UsbAccessory) intent.getParcelableExtra(UsbManager.EXTRA_PERMISSION_GRANTED);

if (intent.getBooleanExtra(UsbManager.EXTRA_PERMISSION_GRANTED, false)) {

// Permission accepted ! We open the communication channels of the accessory !
openAccessory(accessory);

} else {
Log.d(TAG, "permission denied for accessory" + accessory);
}
mPermissionRequestPending = false;
}

// The second action which could have triggered the broadcast receiver
// is the notification that the accessory has been detached from Android device.
} else if (UsbManager.ACTION_USB_ACCESSORY_DETACHED.equals(action)) {

// Use this for Android 2.3.3
UsbAccessory accessory = UsbManager.getAccessory(intent);

// Use this for Android 3.1+
//UsbAccessory accessory = (UsbAccessory) intent.getParcelableExtra(UsbManager.EXTRA_PERMISSION_GRANTED);

if (accessory != null && accessory.equals(mAccessory)) {
closeAccessory();
}
} else if (PHOTO_TAKEN_ACTION.equals(action)) {
photoTakenTextView.setText(R.string.photo_taken_message);
} else if (LOG_FILE_WRITTEN_ACTION.equals(action)) {
logTextView.setText(R.string.log_written_message);
}
}
};

// Open the communication channels to the accessory
private void openAccessory(UsbAccessory accessory) {

// Delegate to the USB service method to obtain a FileDescriptor for your accessory.
mFileDescriptor = mUsbManager.openAccessory(accessory);

if (mFileDescriptor != null) {
mAccessory = accessory;

// The FileDescriptor manages the input- output stream used to communicate with your device
FileDescriptor fd = mFileDescriptor.getFileDescriptor();
mInputStream = new FileInputStream(fd);
mOutputStream = new FileOutputStream(fd);
Thread thread = new Thread(null, commRunnable, TAG);
thread.start();
Log.d(TAG, "accessory opened");
} else {
Log.d(TAG, "accessory open fail");
}
}

// Close the communication channels to the accessory
private void closeAccessory() {
try {
if (mFileDescriptor != null) {
mFileDescriptor.close();
}
} catch (IOException e) {
} finally {
mFileDescriptor = null;
mAccessory = null;
}
}

// Thread to manage incoming data from Arduino
Runnable commRunnable = new Runnable() {

@Override
public void run() {
int ret = 0;
byte[] buffer = new byte[3];

while(ret >= 0) {
try {
ret = mInputStream.read(buffer);
} catch (IOException e) {
Log.e(TAG, "IOException : ", e);
break;
}

switch (buffer[0]) {
case COMMAND_ALARM :
if(buffer[1] == ALARM_TYPE_IR_LIGHT_BARRIER) {
final byte alarmState = buffer[2];
final String alarmMessage = getString(R.string.alarm_message, getString(R.string.alarm_type_ir_light_barrier));

runOnUiThread (new Runnable() {
@Override
public void run() {
if (alarmState == ALARM_ON) {
linearLayout.setBackgroundColor(Color.RED);
alarmTextView.setText(alarmMessage);
} else if (alarmState == ALARM_OFF) {
linearLayout.setBackgroundColor(Color.WHITE);
alarmTextView.setText(R.string.alarm_reset_message);
photoTakenTextView.setText("");
logTextView.setText("");
}
}
});
if (alarmState == ALARM_ON) {
takePhoto();
writeToLogFile(new StringBuilder(alarmMessage).append(" - ").append("date").toString());
} else if (alarmState == ALARM_OFF) {
camera.startPreview();
}
}
break;

default:
Log.d(TAG, "unknown msg : " + buffer[0]);
break;
}
}
}
};

// Choose available Camera
private Camera getCamera() {
Camera camera = null;

try {
if (hasFrontCamera) {
int frontCameraId = getFrontCameraId();
if (frontCameraId != -1) {
camera = Camera.open(frontCameraId);
}
}
if ((camera == null) && hasBackCamera) {
camera = Camera.open();
}
} catch (Exception e) {
Log.d(TAG, "Camera could not be initialized", e);
}
return camera;
}

// Get Front Camera Id
private int getFrontCameraId() {
int cameraId = -1;
int numberOfCameras = Camera.getNumberOfCameras();
for (int i = 0; i< numberOfCameras; i++) {
CameraInfo cameraInfo = new CameraInfo();
Camera.getCameraInfo(i, cameraInfo);
if(CameraInfo.CAMERA_FACING_FRONT == cameraInfo.facing) {
cameraId = i;
break;
}
}
return cameraId;
}

// Take Photo method
private void takePhoto() {
if(camera != null) {
camera.takePicture(null, null, pictureTakenHandler);
}
}

// Picture Callback Handler
private PictureCallback pictureTakenHandler = new PictureCallback() {

@Override
public void onPictureTaken(byte[] data, Camera camera) {
writePictureDataToFile(data);
}
};

// Write to log file method
private void writeToLogFile(String logMessage) {
File logFile = getFile("ProjectThirteenLog.txt");

if (logFile != null) {

BufferedWriter bufferedWriter = null;

try {
bufferedWriter = new BufferedWriter (new FileWriter(logFile, true));
bufferedWriter.write(logMessage);
bufferedWriter.newLine();
Log.d(TAG, "Written message to file : " + logFile.toURI());
logFileWrittenIntent.send();
} catch (IOException e) {
Log.d(TAG, "Could not write to Log File.", e);
} catch (CanceledException e) {
Log.d(TAG, "LogFileWrittenIntent was cancelled.", e);
} finally {
if (bufferedWriter != null) {
try {
bufferedWriter.close();
} catch (IOException e) {
Log.d(TAG, "Could not close Log File.",e);
}
}
}
}
}

// Write Picture to file method
private void writePictureDataToFile(byte[] data) {
SimpleDateFormat dateFormat = new SimpleDateFormat("yyyy-MM-dd-HH-mm-ss");
String currentDateAndTime = dateFormat.format(new Date());
File pictureFile = getFile(currentDateAndTime + ".jpg");
if(pictureFile != null) {
BufferedOutputStream bufferedOutputStream = null;
try {
bufferedOutputStream = new BufferedOutputStream (new FileOutputStream(pictureFile));
bufferedOutputStream.write(data);
Log.d(TAG, "Written picture data to file : " + pictureFile.toURI());
photoTakenIntent.send();
} catch (IOException e) {
Log.d(TAG,"Could not write to Picture File.", e);
} catch (CanceledException e) {
Log.d(TAG, "photoTakenIntent was cancelled.", e);
} finally {
if(bufferedOutputStream != null) {
try {
bufferedOutputStream.close();
} catch (IOException e) {
Log.d(TAG, "Could not close Picture File.",e);
}
}
}
}
}

// File management method
private File getFile(String fileName) {
File file = new File(getExternalDir(), fileName);
if (!file.exists()) {
try {
file.createNewFile();
} catch (IOException e) {
Log.d(TAG, "File could not be created.",e);
}
}
return file;
}

// Storage device management method
private File getExternalDir() {

// Returns the current state of the primary "external" storage device.
String state = Environment.getExternalStorageState();

//Storage state if the media is present and mounted at its mount point with read/write access.
if (Environment.MEDIA_MOUNTED.equals(state)) {
return getExternalFilesDir(null);
} else {
return null;
}
}
}

package com.m2m.projectthirteen;

import java.io.IOException;
import android.content.Context;
import android.hardware.Camera;
import android.util.Log;
import android.view.SurfaceHolder;
import android.view.SurfaceView;

public class CameraPreview extends SurfaceView implements SurfaceHolder.Callback {

private static final String TAG = CameraPreview.class.getSimpleName();
private SurfaceHolder mHolder;
private Camera mCamera;

public CameraPreview(Context context, Camera camera) {
super(context);
mCamera = camera;

// Add a SurfaceHolder.Callback so we get notified when the
// underlying surface is created.

mHolder = getHolder();
mHolder.addCallback(this);

// deprecated setting, but required on Android versions prior to 3.0
mHolder.setType(SurfaceHolder.SURFACE_TYPE_PUSH_BUFFERS);
}

@Override
public void surfaceCreated(SurfaceHolder holder) {
try {
mCamera.setPreviewDisplay(holder);
mCamera.setDisplayOrientation(90);
mCamera.startPreview();
} catch (IOException e) {
Log.d(TAG, "Error setting camera preview : " + e.getMessage());
}
}

@Override
public void surfaceChanged(SurfaceHolder holder, int format, int width, int height) {
// TODO Auto-generated method stub
}

@Override
public void surfaceDestroyed(SurfaceHolder holder) {
// TODO Auto-generated method stub
}
}

Result